## Slide 1
Shift Registers and Memories
LAURINE OWINO (LAMOY)

## Slide 2
Basic memory elements capable of storing one bit in a digital system.
Types:
  D flip-flop
  R-s flip-flop
  J-K flip-flop
  T flip-flop
Flip-Flops

## Slide 3
Shift Registers
Digital device for data storage and and transfer - data is entered then shifted out
Links between main digital system and I/O channels
Constructed by flip-flops. Number of flip-flops defines the size of the register

## Slide 4
SERIAL IN SERIAL OUT
PARALLEL IN PARALLEL OUT
SERIAL IN PARALLEL OUT
PARALLEL IN SERIAL OUT
UNIVERSAL
Types of Shift Registers
SERIAL IN PARALLEL OUT

## Slide 5
Semi-conductor Memories
  Larger systems use SC chips which are made of an array of memory cells.
  Made of flip-flops which are Bipolar, MOS, CMOS.
  Two types:
  RAM
  ROM
  Can be used to store programmed instructions and data.

## Slide 6
  Volatile
  Temporary storage of programs
  Types:
  SRAM
  DRAM
  Not volatile
  Used to store data that is not to change e.g startup programs
  Types:
  Mask Programmed RO
  PROM
  EPROM
  EEPROM
RAM
R0M

## Slide 7
Memory in Arduino
FLASH MEMORY
Stores arduino sketch; program image and any initialized data.
ATMega 128-32k
ATMega 2560-256k
SRAM
Where sketch creates and manipulates variables.
Is made of 3 parts: static data, heap, stack.
EEPROM
Where you can store long-term data.
ATMega 128-1k
ATMega 2560-4k
ATMega 128-2k
ATMega 2560-8k

## Slide 8
Laurine Owino (Lamoy)
Electrical and Electronics Engineering Student, 5th year.
Cyber-security and hardware/firmware enthusiast